## Slide 1: Lab 10
CSE 2301 – Fall 2024

## Slide 2: Weekly News
Exam 2 Grades will be published this week

## Slide 3: INTRODUCTION: SEQUENCE DETECTION
This lab’s primary objective is to build a circuit that shows how we can detect a specified sequence of bits in a data stream.
In this lab you will build a sequence detector that detects ‘010’ and ‘101’ using D Flip-Flops. However, this cannot be done by simply storing the inputs and reading C’BA' or CB’A. Instead, the output should be determined by state transitions.

## Slide 4: Review: Sequence diagrams
You will be looking for a pattern of bits that can be represented by arrows on a state diagram. The arrows will have associated inputs. That’s your first task – to create the state diagram.
How many states do you need?
Will it be with or without overlap?
Detector 01 or 10: A Moore machine
Moore Machine: Output is a function of state only

## Slide 5: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
N/A
We’ll start by adding an initial state (no inputs have been given yet, so no pattern has been stored.

## Slide 6: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
N/A
S1/0
‘0’
0
Consider the ‘0’ input. This is the first bit in the sequence, so we’ll make a new node for it.
We’ll start by adding an initial state (no inputs have been given yet, so no pattern has been stored.

## Slide 7: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
N/A
S1/0
‘0’
0
1
Consider the ‘1’ input. This is not the first bit in the sequence, so we stay in the initial state.
Consider the ‘0’ input. This is the first bit in the sequence, so we’ll make a new node for it.

## Slide 8: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
N/A
S1/0
‘0’
0
1
Consider the ‘1’ input. This is not the first bit in the sequence, so we stay in the initial state.
Continue to state 1 (S1). Evaluate what happens at this node when a ‘0’ occurs or a ‘1’ occurs. Notice that if we get another 0, we just stay in the S1 state, otherwise we move on.
S2/0
‘01’
0
1

## Slide 9: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
N/A
S1/0
‘0’
0
1
Continue to state 1 (S1). Evaluate what happens at this node when a ‘0’ occurs or a ‘1’ occurs. Notice that if we get another 0, we just stay in the S1 state, otherwise we move on.
S2/0
‘01’
0
1
Evaluate S2. This time, if we get a ‘1’, we must start over, because ‘11’ is nowhere in the sequence.
S3/0
‘010’
0
1

## Slide 10: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
S1/0
‘0’
0
1
S2/0
‘01’
0
1
Evaluate S2. This time, if we get a ‘1’, we must start over, because ‘11’ is nowhere in the sequence.
S3/0
‘010’
0
1
Evaluate S3. We complete the sequence. Recognize that you don’t need to add another state for ‘0101’. The point is to output 1, not end up at a “final state”. In this case there’s overlap, so we can return to S2 (in this manner, the sequence would be detected twice from 010101).
1
0
S4/1
‘0101’
0
1

## Slide 11: Review: detecting a sequence
Let’s do an example with the code 0101.
S0/0
S1/0
‘0’
0
1
S2/0
‘01’
0
1
Evaluate S2. This time, if we get a ‘1’, we must start over, because ‘11’ is nowhere in the sequence.
S3/0
‘010’
0
1
Evaluate S3. We complete the sequence. Recognize that you don’t need to add another state for ‘0101’. The point is to output 1, not end up at a “final state”. In this case there’s overlap, so we can return to S2 (in this manner, the sequence would be detected twice from 010101).
1
0
S4/1
‘0101’
0
1
This sequence can be detected with 5 states (4 states if we design a Mealy machine, see the next slide), which means we would only need 3 D flip-flops. Specifically, each state can be represented by a binary code, so S0 would be 000, S1 -> 001, S2 -> 010, and so on.
You can use this information to make the transition table…

## Slide 12: Review: detecting the same sequence: A Mealy machine
Let’s do an example with the code 0101.
And we’re done! This sequence can be detected with only 4 states, which means we would only need two D flip-flops. Specifically, each state can be represented by a binary code, so S0 would be 00, S1 -> 01, S2 -> 10, and S3 -> 11.
You can use this information to make the transition table…
S0:
N/A
S1:
‘0’
0/0
1/0
S2:
‘01’
0/0
1/0
S3:
‘010’
0/0
1/0
1/1
0/0

## Slide 13: Your Task: Sequence ‘010’ and ‘101’
Create the state diagram for sequence detection. You should get 7 states, with one initial state. (Moore Machine)
Recall that we are NOT storing the sequence directly.
**This is part of the sequence diagram you’ll be making.
> How can it be expanded to output ‘1’ when it detects the full
sequence?
> Remember that every node should have two outgoing edges!
N/A
A
D
E
B
1
0
1
0

## Slide 14: Your Task: TRANSITION TABLE
Make a transition table based on the sequence diagram. Depending on how you name each state, you may have different results than your peers. You should have 3 D flip-flops, so your variables will be QC, QB, QA, QC+, QB+, QA+, X (input), and Y (output).
After this, use K-maps to reduce the equations for QC+, QB+, QA+, and Y so that you can build the circuit.
Current |  |  | Next |  | Output
QA | QB | X | QA+ | QB+ | Y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
**Your table will be different

## Slide 15: Other notes DEMO and REPORT
When you demo, you only need one LED (Y output), but it’s recommended that you have 3 additional LEDs for checking your D flip-flops (to debug).
Standard report for this assignment.