## Slide 1: Lab 12: VHDL
CSE 2301 – Fall 2024

## Slide 2: Introduction: overview
Today’s Lab will include a lecture and an assignment
You will be learning the basics of VHDL and re-creating two previous labs in VHDL, the 2 Bit ALU and the Hamming Code Generator
Contrast the difficulty of these labs with how easily they are implemented in VHDL
You will be given significant starter code

## Slide 3: VHDL : VHSIC Hardware Description Language
Specialized language for designing and simulating hardware systems
  Used in domains of PLA programming, PCB design, and integrated circuit design
Design paradigms for both combinational and sequential circuits

## Slide 4: Combinational Design
Consider the following combinational circuit
The equations for the outputs are: Q = AB’ + A’B QN = (AB’ + A’B)’ = Q’

## Slide 5: Combinational VHDL

## Slide 6: Combinational VHDL: Assignment (the important slide)
Focus on the red boxed section of code
The symbol <= is for assignment; The signal on the left will be set to the expression on the right.
In VHDL, there is no concept of order, the first statement won’t always execute before the last.
Instead, all signals are updated constantly and concurrently
When input A is changed, the value of X and Q are updated simultaneously, in any order

## Slide 7: Combinational VHDL: Assignment
Valid keywords include:
  Logical: and, or, not, nand, nor, xor, xnor
  Arithmetic: +, -, *, /, **
  Shift: sll, srl, sla, sra
  Concatenation: & ex: “01” & “10” returns “0110”
To assign a literal to a…
  Signal: use single quotes e.g. x <= ‘1’
  Vector: use double quotes e.g. x <= “0011”

## Slide 8: Combinational VHDL: Library
Libraries give us access to additional functions
  std_logic_1164 contains std_logic and std_logic_vector and related functions
  IEEE.numeric_std.all allows us to use arithmetic operators

## Slide 9: Combinational VHDL: Entity
You will not be responsible for this part of the program
Defines the input and output interface of the part
std_logic represents a 1 bit signal, which can be ‘0’ or ‘1’
std_logic_vector represents a multi-bit signal of any length like “01” or “0001100001111111”

## Slide 10: Combinational VHDL: ARCHITECTURE
You will not be responsible for most of this part of the program
Before the “begin” keyword, extra signals are defined
  These are internal signals which are not inputs or outputs
After the “begin” keyword, the behavior of the part is defined
Again, the order of signals does not matter, and the statements will continuously execute forever

## Slide 11: Combinational VHDL: MUX example
This VHDL program implements a 4:1 MUX

## Slide 12: Combinational VHDL: MUX entity
This VHDL program implements a 4:1 MUX
The entity portion defines 2 inputs and 1 outputs
D is a 4 bit input; SEL is a 2 bit input; Q is a 1 bit output
Single bits from vectors can be accessed with parenthesis
  The rightmost bit of D is D(0); the leftmost bit is D(3)

## Slide 13: Combinational VHDL: Processes
This VHDL program implements a 4:1 MUX
Processes are like functions
The signals in parenthesis after process are the Sensitivity List
The process will run whenever one of the signals in the sensitivity list changes
If statements may only be used inside processes

## Slide 14: Combinational VHDL: Processes
This VHDL program implements a 4:1 MUX
Processes are sequential… kind of
Take for example: process (y) begin x <= ‘1’; y <= ‘x’; end process;
If x has a value of 0 when the process begins executing, the value of y after the function finishes is 0, not 1.
Fix this by adding x to the sensitivity list of the process so that the process will execute twice

## Slide 15: Combinational VHDL: Extra Notes
Signal lengths need to match
Take for example
If Q is a 4 bit signal, and A and B are 2 bit signals, A and B need to be padded to be 4 bits using extra 0s. This is accomplished using the concatenation operator.
In order to use the arithmetic operators, A and B need to be converted to unsigned integers. Use the unsigned function to convert bit vectors to unsigned integers.

## Slide 16: Part 1: PARITY bit generator
We will be implementing an even parity bit generator
Parity Bit | Based on Data Bits
P1 | D(3), D(2), D(0)
P2 | D(3), D(1), D(0)
P3 | D(2), D(1), D(0)

## Slide 17: REVIEW: hamming code
Hamming codes add parity bits for error checking. With the hamming distance seen here (3), we can check for and correct one error.
Note the names we give the parity and data bits here. They represent weights.
Bit positions
Parity bit positions - interspersed
P1
P2
P4
Q(6)
D(3)
D(2)
D(1)
D(0)
Weighted 4-bit data word
Q(5)
Q(4)
Q(3)
Q(2)
Q(1)
Q(0)

## Slide 18: Part 1: PARITY BIT generator
The truth table shows how you might reduce the equation to determine the output of each parity bit based on three inputs (as described on the previous page).
This seems overly complicated, doesn’t it?
3 data bits |  |  | Even parity bit
X | Y | Z | P
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
P = X’Y’Z + X’YZ’ + XY’Z’ + XYZ

## Slide 19: Part 1: PARITY bit generator
Using some Boolean algebra, we can simplify this greatly. This leads to a lemma of sorts: the XOR of multiple variables will tell us whether their sum is even (0 if even, 1 if odd).
P = X’(Y’Z + YZ’) + X(Y’Z’ + YZ)
= X’(Y Z) + X(Y Z)’
= X Y Z

## Slide 21: Part 2: BASIC ALU
Your task is to reimplement the ALU from lab 5 in VHDL. An Arithmetic Logic Unit performs different functions based on the provided selector input.
The ALU should be able to perform AND, OR, addition, and multiplication operations on two 2-bit binary inputs.
Do NOT implement these functions using logic gates, use the built in VHDL arithmetic operators

## Slide 23: Starter Code
Starter code is provided for each file, you should only need to add code where indicated
None of this content was covered in lecture, so ask for help frequently

## Slide 24: Follow Along
Click File->New

## Slide 25: Follow Along
Click Model Wizard -> Ok

## Slide 26: Follow Along
Click:
  Create a new, empty model
  Create a new symbol with the specified model attached
  Next

## Slide 27: Follow Along
Click VHDL
Name the model
Click Next

## Slide 28: Follow Along
Create an input D with:
  Function: Input
  Name: D
  Left Bit Number: 3
  Right Bit number: 0
Click <<Add Vector; NOT <<Add Single Bit
Do not click next yet

## Slide 29: Follow Along
Create an input D with:
  Function: Output
  Name: Q
  Left Bit Number: 6
  Right Bit number: 0
Click <<Add Vector; NOT <<Add Single Bit
Click Next

## Slide 30: Follow Along
Ensure D is a left pin and Q is a right pin
Then click next

## Slide 31: Follow Along
Click New Lib…

## Slide 32: Follow Along
Name the library and click Save

## Slide 33: Follow Along
Select the new library and click Finish

## Slide 34: Follow Along
Save the VHDL file

## Slide 35: Follow Along
Click File -> Open

## Slide 36: Follow Along
Select the dwv file you just saved, and click Open

## Slide 37: Follow Along
Select the dwv file you just saved, and click Open

## Slide 38: Follow Along
Delete everything currently in the file

## Slide 39: Follow Along
Paste in the starter code

## Slide 40: Complete part 1
Add your code for P1 P2 and P3 where the comments indicate
Use the ctrl-Q shortcut to compile the code

## Slide 41: Follow along
Use file -> New -> Circuit -> OK to create a new empty circuit

## Slide 42: Follow along
Use file -> New -> Circuit -> OK to create a new empty circuit

## Slide 43: Follow along
Create the following circuit to test your VHDL
To create the breakouts, right click on the blue bus wires and click breakout
Use pin spacing of 4 for both breakouts

## Slide 44: Follow along
Click Simulation -> reset simulation to clear the C values and test the VHDL component

## Slide 45: Follow along
Use the same process to create the ALU_2 part
Use the ports on this slide

## Slide 46: Follow along
Use the same process to create the ALU_2 part
Use the circuit layout on this slide